## Slide 1
Robotic Seminar
Second meeting 28-Nov
Mingyuan Chi

## Slide 2
RGB
Nerf2real: Sim2real transfer of vision-guided bipedal motion skills using neural radiance fields
Neural Field
Sensor : Camera(Phone)
Limitation:
1. manual postprocessing is required, (minimally textured area)
2. Should sperate process static scene and dynamic objects
3. high cost of NeRF
Advantage:
1. NeRF significantly reduces the sim2real gap with realistic scene renderings
2. videos from commodity mobile devices to create realistic simulations. This makes the system accessible and practical, as it doesn't require specialized hardware.

## Slide 3
RGB
UniSim: A Neural Closed-Loop Sensor Simulator
Neural Field
Sensor : Camera & LiDAR
Limitation:
1. requires LiDAR
2. complex pipeline
Advantage:
1. using voxel rendering to leverage the computational cost
2. produce higher-fidelity LiDAR simulation with less noise
3. closed loop simulation

## Slide 4
RGB
SurfelGAN: Synthesizing Realistic Sensor Data for Autonomous Driving
Synthetic Dataset
Sensor: Camera & LiDAR
Purpose : Generate
realistically looking
camera images (Texture)
Method :
Surfel : A surfel is a small, oriented disk used to represent a portion of a 3D surface.
Advantage :
1. the first to build purely data-driven camera simulation system for autonomous driving.
2. High realism
Limitation:
1. SurfelGAN unable to recover from broken geometry
2. Place where surfel map does not cover will cause Hallucination
3. complex training process(Semantic Segmentation, Instance Segmentation)

## Slide 5
RGB
SurfelGAN: Synthesizing Realistic Sensor Data for Autonomous Driving
Synthetic Dataset
Surfel(surface element) : A surfel is a small, oriented disk used to represent a portion of a 3D surface.

## Slide 6
RGB
Real2Sim2Real: Self-Supervised Learning of Physical Single-Step Dynamic Actions for Planar Robot Casting
Synthetic Dataset
PRC : Planar Robot Casting
Advantage :
1. self supervised, no manual data labeling and intervention
2. efficient learning from few physical examples (sim + real)
Limitation :
1. harder to extend to 3D , inherent uncertainty about static and dynamic friction

## Slide 7
RGB
Reinforcement and Imitation Learning for Diverse Visuomotor Skills
Simulation Manually Adjusted
a Kinect camera (RGBD) was visually calibrated to match the position and orientation of the simulated camera, and the simulation’s dynamics parameters were manually adjusted to match the dynamics of the real arm.
GAIL : Generative Adversarial Imitation Learning
Advantage :
1. reinforcement learning + limitation learning
2. diverse task from small amount of human demonstration data
Limitation :
1. Reality Gap in Sim2Real Transfer
2. simulation’s dynamics parameters were manually adjusted

## Slide 8
Depth
LiDAR : determining ranges by targeting an object or a surface with a laser and measuring the time for the reflected light to return to the receiver .
Kinect : the motion sensing device for the Xbox 360 gaming console. It provides RGB, Infra-Red (IR), depth, skeleton, and audio streams to an application.
Zed Camera : neural depth, built-in IMU
RealSense : long range depth camera, built-in IMU
Sensors

## Slide 9
Depth
Sim2Real Neural Controllers for Physics-Based Robotic Deployment of Deformable Linear Objects
Naive
Sensor : realsense
Limitation :
- precision is not that good
- it's task specified , not generalized
Advantage :
- simple architecture but effective
DLO : Deformable linear objects

## Slide 10
Depth
LiDAR Data Noise Models and Methodology for Sim-to-Real Domain Generalization and Adaptation in Autonomous Driving Perception
Domain Randomization
Advantage :
- naive but effective
Limitation :
- assumption of Gaussian additive model(Noise Model) and Bernoulli distribution approximation(Point Dropout Model)

## Slide 11
Depth
LiDAR Sensor modeling and Data augmentation with GANs for Autonomous driving
Realistic Simulation
Advantage:
- formulize the sensor modeling as image2image translation
- easy pipeline
Limitation:
- NST requires workarounds via heuristics to feed the style with every frame generation.

## Slide 12
Depth
Unsupervised Neural Sensor Models for Synthetic LiDAR Data Augmentation
Data Augmentation
Advantage :
1. two available generator
Limitation :
1. highly depend on cycleGAN and NST

## Slide 13
Depth
Towards Zero Domain Gap: A Comprehensive Study of Realistic LiDAR Simulation for Autonomy Testing
Simulation Enhancement
Advantage :
- Comprehensive Analysis of LiDAR Phenomena
Limitation :
- Focus on Analysis Rather Than Solution

## Slide 14
Depth
Characterizations of Noise in Kinect Depth Images: A Review
Kinect Survey

## Slide 15
Depth
Sim2Real2Sim: Bridging the Gap Between Simulation and Real-World in Flexible Object Manipulation
Realistic Simulation
Advantage :
- simulation has real world feedback
Limitation :
- The strategy, while effective, is specifically developed for flexible object manipulation.

## Slide 16
IMU
Sim-to-Real Strategy for Spatially Aware Robot Navigation in Uneven Outdoor Environment
Policy Modal
point cloud is gained from LiDAR
DWA: Dynamic Window Approach to penalize velocities that could cause robot flip-overs
IMU is processed by PCA
Advantage :
- avoid potential noise in the IMU signal
Limitation :
- The current formulation of the robot's navigation system does not include the capability to avoid rough terrains

## Slide 17
IMU
Policies Modulating Trajectory Generators
Policy Modal
IMU as modal for policy
Advantage :
- IMU signal coupled in the policy network
Limitation :
- The current approach relies on trajectory generators chosen based on intuition rather than a systematic method.
- only IMU, motor position information

## Slide 18
IMU
Sim-to-Real Strategy for Spatially Aware Robot Navigation in Uneven Outdoor Environment
Policy Modal
IMU as modal input for policy
Advantage :
- IMU signal coupled in the policy network
- Multi-Modal information
Limitation :
- asynchronous multi-modal inputs for RL policies

## Slide 19
IMU
Zero-Shot Policy Transferability for the Control of a Scale Autonomous Vehicle
Error Esimation
IMU for error estimation
Advantage:
- explainable coupled with IMU signal
Limitation :
- naive control
- IMU signal is assumed to be exact

## Slide 20
IMU
Learning Autonomous Mobility Using Real Demonstration Data)
Controller Modal
Time sequence IMU modeling with NN
Advantage :
- considering the time sequence influence of the IMU signal
Limitation :
- not coupled with policy, only the acuators controller

## Slide 21
Force Sensor
Robotic tactile perception of object properties: A review
Review
Single-point contact sensor :
  measure contact force : ATI Nano 17 force-torque sensor
  measure vibration : biomimeticwhiskers
Tactile Array: fiber optics, MEMS barometers, RoboTouch, DigiTacts
optical tactile sensor, high resolution : GelSight, GelTip, TacTip, DIGIT

## Slide 22
Force Sensor
Touch driven controller and tactile features for physical interactions
Jacobian feed forward
Advantage :
- numerical robust
- fast
Limitation :
- not precise enough
- limit to specific contact configuration

## Slide 23
Force Sensor
Generation of GelSight Tactile Images for Sim2Real Learning
Simulation Enhancement
Advantage :
- high resolution
- easy to implement, fast
Limitation :
- Based on the modeling accuracy

## Slide 24
Force Sensor
Learning the sense of touch in simulation: a sim-to-real strategy for visionbased tactile sensing
FEM Simulation
figure a is corresponding to paper "Ground Truth Force Distribution for Learning-Based Tactile Sensing: A Finite Element Approach”
DIS: Dense Inverse Search (Fast Optical Flow using Dense Inverse Search)
Advantage :
- FEM simulation is more precise
Limitation :
- the training result is related to the FEM accuracy

## Slide 25
Force Sensor
Skill generalization of tubular object manipulation with tactile sensing and Sim2Real learning
Simulation Enhancement
Advantage :
- use a anglenet to extract angle information from tactile information
Limitation :
- the modeling of DIGIT is fully depend on Gazebo

## Slide 26
Force Sensor
Sim-to-Real for Robotic Tactile Sensing via Physics-Based Simulation and Learned Latent Projections
FEM Simulation
Advantage :
- 75 faster than previous model
Limitation :
- linear elasticity is not accurate enough

## Slide 27
Encoders
Control Transformer: Robot Navigation in Unknown Environmentsthrough PRM-Guided Return-Conditioned Sequence Modeling
Position Esitmation
Advantage :
- effect in complex environment (for policy)
Limitation :
- assume encoders are correct, and use that to compute the error

## Slide 28
Encoders
NeuronsGym: A Hybrid Framework and Benchmark for Robot Tasks with Sim2Real Policy Learning
Uncertainty Estimation
A simulator framework

## Slide 29
Encoders
LiDAR SLAM with a Wheel Encoder in a Featureless Tunnel Environment
Sensor Fusion
use wheel encoder to correct the LiDAR data, but not related to simulation
Advantage :
- combine IMU, Encoders, LiDAR using extended Kalman Filter
Limitation :
- the algorithm is only validated in flat and inclined terrian

## Slide 30
Next Week
Add papers/ delete articles according to today’s assesments
Write report draft and send it by email by the end of 5th Dec