## Slide 1
Robotic Seminar
Second meeting 12-Dec
Mingyuan Chi
Sensor Modeling in Sim2Real

## Slide 2
RGB camera
Depth sensor
IMU
Force sensor
Encoders

## Slide 3
RGB
Reinforcement and Imitation Learning for Diverse Visuomotor Skills
Simulation Manually Adjusted
a Kinect camera (RGBD) was visually calibrated to match the position and orientation of the simulated camera, and the simulation’s dynamics parameters were manually adjusted to match the dynamics of the real arm.
GAIL : Generative Adversarial Imitation Learning
Notes: CNN + LSTM to handle the information from camera
intuitive
Gray part is the policy
Others are simulation
Advantage:
It could learn from the past (LSTM)

## Slide 4
RGB
Nerf2real: Sim2real transfer of vision-guided bipedal motion skills using neural radiance fields
Neural Field
Sensor : Camera(Phone)
Notes: Advantage:
High precision from Nerf
Easy to construct the environment (a generic phone)
Disadavantage
Manual postprocessing
Long time processing and high computational intensity
- COLMAP: 3-4h
- Nerf : 20min on 8 V100 GPU
- Policy : 24h
3. Dynamic (MuJoCo)-Static(Nerf) Object seperation

## Slide 5
RGB
UniSim: A Neural Closed-Loop Sensor Simulator
Neural Field
Sensor : Camera & LiDAR
Notes: Simulation Environment
Relation to Last Work:
1. Neural Scene
Advantage:
1. Less complexity (without training a Nerf)
2. couple dynamic objects and static objects
Neural Sensor
CNN modeling
Closed loop simulation

## Slide 6
RGB
SurfelGAN: Synthesizing Realistic Sensor Data for Autonomous Driving
Synthetic Dataset
Sensor: Camera & LiDAR
Purpose : Generate
realistically looking
camera images (Texture)
Surfel : A surfel is a small, oriented disk used to represent a portion of a 3D surface.
Notes: Beyond environment creation,
Surfel is gained from LiDAR
SurfelGAN : (Surfel Rendered image + Segmentation) -> 2D camera image
Pupose: generate realistic image
Limitation :
1. unable to recover from broken geometry
2. Hallucination : surfel map doesn’t cover

## Slide 7
RGB
Real2Sim2Real: Self-Supervised Learning of Physical Single-Step Dynamic Actions for Planar Robot Casting
Synthetic Dataset
PRC : Planar Robot Casting
Notes: Relationship To Last Work:
Dataset Augmentation
Pipeline :
first, generate a bunch of real world interactive dataset
second, sample a subset from it, and optimize the parameters in the simulation to close the gap between.
third, generate a bunch of simulation interactive dataset
last, combine reald interactive dataset and simulation interactive dataset to train the policy
Advantage:
1. simple and efficient
Limitation ：
1. can hard to extend to other task (Planar Robot Casting)

## Slide 8
Depth
LiDAR : determining ranges by targeting an object or a surface with a laser and measuring the time for the reflected light to return to the receiver .
Kinect : the motion sensing device for the Xbox 360 gaming console. It provides RGB, Infra-Red (IR), depth, skeleton, and audio streams to an application.
Zed Camera : neural depth, built-in IMU
RealSense : long range depth camera, built-in IMU
Sensors

## Slide 9
Depth
Towards Zero Domain Gap: A Comprehensive Study of Realistic LiDAR Simulation for Autonomy Testing
Simulation Enhancement
Notes: Uncertainty Phenomenon
Unreturned pulse because of fast amplitude decay
Multiple echos caused by multiple surfaces
Spurious returns caused by beam divergence
Noisy points caused by ambiguity in wavepeak

## Slide 10
Depth
LiDAR Data Noise Models and Methodology for Sim-to-Real Domain Generalization and Adaptation in Autonomous Driving Perception
Domain Randomization
Notes: Noise model
gaussian distribution
deviation of the gaussian model
Point dropout model
Bernoulli distribution
Quadratic polynomial

## Slide 11
Depth
LiDAR Sensor modeling and Data augmentation with GANs for Autonomous driving
Realistic Simulation
Sensor: LiDAR
Notes: Neural Network Modeling
Similar to SurfelGAN
Model the transition from simulated LiDAR to sim LiDAR using Cycle GAN
Generate high realistic LiDAR

## Slide 12
Depth
Unsupervised Neural Sensor Models for Synthetic LiDAR Data Augmentation
Data Augmentation
Notes: Futher from (same author) last work
Here, they use a general generation model which can be CycleGAN, Neural Style Transfer
The total trainig dataset is the combination of realistic dataset and augmented dataset

## Slide 13
Depth
Characterizations of Noise in Kinect Depth Images: A Review
Kinect Survey
Notes: There is also a work provide the sensor modeling for Kinect.
Based on these modeling, they could sperate the noise into three categories

## Slide 14
Depth
Sim2Real2Sim: Bridging the Gap Between Simulation and Real-World in Flexible Object Manipulation
Realistic Simulation
Notes: The work sim2real2sim focus on DRC(DARPA Robotics Challenge) Plug task
They use a visual servoing approach, which uses the reverse Jacobian of the difference between preinsert frame and cable tip frame to align the pose. Therefore, it could update the parameters in the simulation.

## Slide 15
Depth
Sim2Real Neural Controllers for Physics-Based Robotic Deployment of Deformable Linear Objects
Naive
DLO : Deformable linear objects
Notes: As for the modern camera, Realsense
This work focus on Deformed Linear Objects Problem.
The 3D position of the nodes on the linear objects are directly gained from the RealSense camera

## Slide 16
IMU
Policies Modulating Trajectory Generators
Policy Modal
Sample at a certain freqeuncy
Notes: Interial Measurement Unit is primarily used for measuring acceleration.
It’s always used with other sensors like RGBD cam and encoders.
The signal frequencies are different.
Constant frequency sampling. -> policy network
Loss the information in the interval

## Slide 17
IMU
Learning Autonomous Mobility Using Real Demonstration Data)
Controller Modal
Butterworth loss-pass filter with 15Hz to denoise and outlier removal
LSTM interpret time-seq signals
Notes: To better use the high frequency signal
Butterworth low-pass filter with 15Hz to denoise and outlier removal.
LSTM controller to interpret these time-seq signals
The policy could only work at a low frequency

## Slide 18
IMU
Sim-to-Real Strategy for Spatially Aware Robot Navigation in Uneven Outdoor Environment
Policy Modal
Observation buffer
Notes: Visual observation buffer, which buffer the depth information to make it synchronous with IMU signals
High frequency.

## Slide 19
IMU
Sim-to-Real Strategy for Spatially Aware Robot Navigation in Uneven Outdoor Environment
Policy Modal
Extract surface vibration using PCA (first two principle components)
DWA: Dynamic Window Approach to penalize velocities that could cause robot flip-overs
Notes: Extract information from IMU
Extract surface vibration using PCA
First two principle components.
Dynamic Window Approach penalize velocity prevent from flip-over.

## Slide 20
IMU
Zero-Shot Policy Transferability for the Control of a Scale Autonomous Vehicle
Error Estimation
IMU for error estimation
Advantage:
- explainable coupled with IMU signal
Limitation :
- naive control
- IMU signal is assumed to be exact
Notes: IMU -> heading information
Extract error state combined with GPS signals
IMU -> EKF
Error state-> model predictive controller -> navigation accuracy

## Slide 21
Force Sensor
Robotic tactile perception of object properties: A review
Review
Single-point contact sensor :
  measure contact force : ATI Nano 17 force-torque sensor
  measure vibration : biomimeticwhiskers
Tactile Array: fiber optics, MEMS barometers, RoboTouch, DigiTacts
optical tactile sensor, high resolution : GelSight, GelTip, TacTip, DIGIT

## Slide 22
Force Sensor
Touch driven controller and tactile features for physical interactions
Jacobian feed forward
Notes: The traditional way to model tactile array
Numerical approach
Contact pattern -> Jacobian -> controller system
Numerical robust
Contact pattern should be computed manually

## Slide 23
Force Sensor
Sim-to-Real for Robotic Tactile Sensing via Physics-Based Simulation and Learned Latent Projections
FEM Simulation
Notes: Specialized shape sensor : SynTouch BioTach
Two VAE -> Two Latent Space -> Two MLP bridge the gap between two latent spaces
FEM is of high accuracy, it could measure any contact pattern

## Slide 24
Force Sensor
Generation of GelSight Tactile Images for Sim2Real Learning
Simulation Enhancement
Sensor : GelSight
Simulator : Gazebo
Notes: As for optical tactile,
Deformation – rendering model
Gaussian filter -> strain membrain.
Phong’s shading render the image.
Forward method
Fast and robust
Not accurate enough

## Slide 25
Force Sensor
Learning the sense of touch in simulation: a sim-to-real strategy for visionbased tactile sensing
FEM Simulation
figure a is corresponding to paper "Ground Truth Force Distribution for Learning-Based Tactile Sensing: A Finite Element Approach”
DIS: Dense Inverse Search (Fast Optical Flow using Dense Inverse Search)
Notes: FEM could also be used here.
What we need is to use a model as a transition between the FEM simulation and the real world observation.
First method, force distribution
Second method , optical flow + force distribution

## Slide 26
Force Sensor
Skill generalization of tubular object manipulation with tactile sensing and Sim2Real learning
Simulation Enhancement
Sensor : DIGIT
SAC : Soft Actor-Critic
TCP : Tool Center Point
Notes: Specific Task: In-hand pose of tubar objects.
The transformation could also be learned using a CycleGAN.
CycleGAN-like architecture model the transformation from simulated image to realistic representation

## Slide 27
Encoders
NeuronsGym: A Hybrid Framework and Benchmark for Robot Tasks with Sim2Real Policy Learning
Uncertainty Estimation
A simulator framework
Notes: Encoders inside motor
Angular velocity , torque -> electrical data
In this simulation framework called NeuraonGym, the encoders are modeled using Guassian noise

## Slide 28
Encoders
LiDAR SLAM with a Wheel Encoder in a Featureless Tunnel Environment
Sensor Fusion
EKF synchronize frequency
Advantage :
- combine IMU, Encoders, LiDAR using extended Kalman Filter
Limitation :
- the algorithm is only validated in flat and inclined terrian
Notes: Encoder signal frequency is different.
EKF to ensure the frequency of the combined singal from IMU and encoders are synchronized

## Slide 29
Thank you